## Slide 1: Development of Computer Vision and Image Processing at NSLS-II
William Watson

## Slide 2: Purpose
Development of image analysis software backed by OpenCV
To provide an easy use python module to access computer vision functions
Optimized results for fast computation, via C++, Intel IPP/TBB
Automate processes from image input such as:
  Positon, spread, and intensity of X-Ray Beams
  Isolating and computing data on multiple objects
  Provide assistance to mounting samples and report any errors

## Slide 3: OpenCV and CVLIB
Small Programs call upon functions in CVLIB
CVLIB calls upon OpenCV, which has a Python Wrapper for C++
OpenCV 3.0 supports optimization via Intel’s IPP Low Level Functions, Intel TBB
Computation is done on a dedicated IBM Image Server
Small Program
CVLIB
OpenCV (Python Wrapper to C++)
Intel IPP/TBB Functions on IBM Server
Optimized Results
Sergey Sivolgin, 2014-08-11 11:25 am

## Slide 4: BPM-1 X-Ray Analysis (IXS)
Images Courtesy of: Yong Cai, Alessandro Cunsolo, Alexey Suvorov, and the IXS Beamline Staff
Purpose:
Discover Position of Beam
Discover Spread of Beam
Discover Intensity of Beam
Discover the Centroid of the Beam
E = 9.1 keV
Scintillator: YAG
Camera: Prosilica
Magnification: 5x

## Slide 5: BPM-1 X-Ray
3rd XBPM
2nd XBPM
1st XBPM
Images Courtesy of: Yong Cai, Alessandro Cunsolo, Alexey Suvorov, and the IXS Beamline Staff
Located in B Hutch (IXS)

## Slide 6: BPM-1 Image Results
Result Superimposed on Original
Thresholding Result
Jet Color Map
Process:
Threshold
Find Contours
Interpret Contour Data (Plot, Draw, and Print)
Images Courtesy of: Yong Cai, Alessandro Cunsolo, Alexey Suvorov, and the IXS Beamline Staff

## Slide 7: BPM-1 Data Results
Console Output:
Object Details:
perimeter: 2356.99022925
orientation: 179.838363647
max: (925, 198)
height: 372
extrema: {'B': (938, 568), 'R': (1054, 415), 'L': (813, 377), 'T': (914, 196)}
area: 65058.5
min: (1047, 564)
sum intensity: 20426526
width: 241
centroid: (933, 382)
mean intensity: 227.842390577
Images Courtesy of: Yong Cai, Alessandro Cunsolo, Alexey Suvorov, and the IXS Beamline Staff

## Slide 8: BPM-1 Results
Use Centroid and Extrema to adjust beam within image
Sum of the Pixels displays the total intensity of the beam
The Maximum point of intensity, and maximum intensity discovered
Area and Perimeter of Beam
Height and Width of the current Beam
Average Intensity of the Beam

## Slide 9: BPM-1 Time
BPM-1 (Single):
Real 0m0.350s
User 0m0.300s
Sys 0m0.068s
Images Courtesy of: Yong Cai, Alessandro Cunsolo, Alexey Suvorov, and the IXS Beamline Staff

## Slide 10: Analysis -Merlin Quad X-Ray Detector (IXS)
Images Courtesy of: Yong Cai, Alessandro Cunsolo, Alexey Suvorov, and the IXS Beamline Staff
Data Retrieved from the Merlin Detector at IXS
Purpose:
Isolate Individual Streaks
Process each Streak to learn Position, Center, Spread, Intensity, Max Values, etc.
Count Intensity in each streak
E = 9.1 keV
Direct detection
PEL size = 55 [um]

## Slide 11: Merlin Image Results
Process:
Convert to Grayscale
Threshold Image
Find and filter contours by size
For each object:
  Print Object’s Data
  Plot Points of Interest
Draw Contours
Apply JET
Images Courtesy of: Yong Cai, Alessandro Cunsolo, Alexey Suvorov, and the IXS Beamline Staff

## Slide 12: Merlin Data Results for First Object (Largest)
Console Output:
Object 1:
perimeter: 125.840619564
orientation: 179.981033325
max: (131, 78)
height: 55
extrema: {'B': (129, 122), 'R': (135, 98),
'L': (126, 92), 'T': (132, 67)}
area: 270.5
min: (134, 83)
sum intensity: 62689
width: 9
centroid: (130, 95)
mean intensity: 126.644444444
Images Courtesy of: Yong Cai, Alessandro Cunsolo, Alexey Suvorov, and the IXS Beamline Staff

## Slide 13: Merlin - Time
Merlin (1 Image Standalone):
Real 0m0.321s
User 0m0.284s
Sys 0m0.036s
Images Courtesy of: Yong Cai, Alessandro Cunsolo, Alexey Suvorov, and the IXS Beamline Staff

## Slide 14: ABBIX Beamlines (AMX): Pins in a Robot Gripper
Pin and Gripper ‘Perfect’ Image
Pin Template Image
Gripper Template Image
Images Courtesy of: Jean Jakoncic, AMX Beamline
Images are from AMX, Displays a Pin and a Gripper, in an attempt to grab the pin

## Slide 15: Robot Gripper - Purpose
Purpose:
Find if Pin is in the Gripper
Determine if Pin is properly mounted
  Analyze the position of the Gripper and Pin within the image
  Find the Region of Interest (ROI) for the Pin and Gripper
  Compare the Pin and Gripper to a ‘Perfect’ Image to determine if anomalies are present
  Advise the user to any potential problems
Images Courtesy of: Jean Jakoncic, AMX Beamline

## Slide 16: Robot Gripper– ‘Perfect’ vs Test Cases
‘Perfect’
Image 1
Image 2
Image 3
Image 4
Images Courtesy of: Jean Jakoncic, AMX Beamline

## Slide 17: Robot Gripper- Results
Console Output:
Template: 0.0 Disim
Image-1: 1.36311088973 Disim
Image-2: 0.0286209618648 Disim
Image-3: 0.0045508842333 Disim
Image-4: 0.190357587177 Disim
‘Perfect’
Image 1
Image 2
Image 3
Image 4
Images Courtesy of: Jean Jakoncic, AMX Beamline

## Slide 18: Robot Gripper Time – 1-19 Images
Chart: Average Time Per Photo
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
Avg | 0.526 | 0.358 | 0.29533 | 0.2665 | 0.2512 | 0.23817 | 0.22857 | 0.22287 | 0.218 | 0.2131 | 0.21127 | 0.20775 | 0.20708 | 0.20536 | 0.20307 | 0.20844 | 0.20118 | 0.19683 | 0.19684
Chart: Total Computation Time
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
Time | 0.526 | 0.716 | 0.886 | 1.066 | 1.256 | 1.429 | 1.6 | 1.783 | 1.962 | 2.131 | 2.324 | 2.493 | 2.692 | 2.875 | 3.046 | 3.335 | 3.42 | 3.543 | 3.74
Number of Images | Total Time | Average Time
1 | 0.526 | 0.526
2 | 0.716 | 0.358
3 | 0.886 | 0.29533333
4 | 1.066 | 0.2665
5 | 1.256 | 0.2512
6 | 1.429 | 0.23816667
7 | 1.6 | 0.22857143
8 | 1.783 | 0.222875
9 | 1.962 | 0.218
10 | 2.131 | 0.2131
11 | 2.324 | 0.21127273
12 | 2.493 | 0.20775
13 | 2.692 | 0.20707692
14 | 2.875 | 0.20535714
15 | 3.046 | 0.20306667
16 | 3.335 | 0.2084375
17 | 3.42 | 0.20117647
18 | 3.543 | 0.19683333
19 | 3.74 | 0.19684211

## Slide 19: Pin/Gripper – ‘Perfect’ vs Test Cases
‘Perfect’
Image 1
Image 2
Image 3
Image 4
Images Courtesy of: Jean Jakoncic, AMX Beamline

## Slide 20: Pin/Gripper Detailed Analysis
Purpose:
Find Pin and Gripper ROI’s
Compare Apparatus to ‘Perfect’ for anomalies
Discover Possible Kinks within image
Discover if Pin is not properly mounted
Discover the Center of Mass
Use Extreme Points as an assist for Alignment, along with Centroid

## Slide 21: Pin/Gripper Image Analysis – Results – Image 1
Match Metrics:
Image Dissimilarity: 1.36080901012
Mount Centroid: Too High: 104
Missing Component / Gripper Not Aligned
Console Output on Image 1:
Image 1:
perimeter: 2017.74725473
max: (745, 1)
height: 217
extrema: {'B': (1203, 218), 'R': (1567, 129),
'L': (745, 114), 'T': (748, 1)}
area: 168731.5
min: (793, 1)
sum intensity: 4280971
width: 822
centroid: (1161, 104)
mean intensity: 23.999971969
Images Courtesy of: Jean Jakoncic, AMX Beamline

## Slide 22: Pin/Gripper Image Analysis – Results – Image 2
Console Output:
Image 2:
perimeter: 3512.21232665
max: (497, 66)
height: 664
extrema: {'B': (1206, 665), 'R': (1450, 31),
'L': (497, 1), 'T': (497, 1)}
aspect ratio: 1.43458646617
area: 532620.5
min: (515, 1)
sum intensity: 30095708
width: 953
centroid: (968, 310)
mean intensity: 47.5601903943
Match Metrics:
Image Dissimilarity: 0.0274253192917
Possible Kinks Detected
41 Possible Kink Points Detected: Adjust Gripper
Possible Kink Distance on R: 115.004347744
Possible Kink Distance on L: 27.3130005675
Pin Not Mounted Correctly: Distance: 329
Images Courtesy of: Jean Jakoncic, AMX Beamline

## Slide 23: Pin/Gripper Image Analysis – Results – Image 3
Console Output:
Image 3:
perimeter: 3272.13917053
max: (496, 1)
height: 677
extent: 0.902237973263
extrema: {'B': (593, 678), 'R': (1452, 189),
'L': (496, 22), 'T': (503, 1)}
area: 585413.5
min: (525, 1)
sum intensity: 20199272
width: 956
centroid: (974, 323)
mean intensity: 31.2096685476
Match Metrics:
Image Dissimilarity: 0.00487836456791
Images Courtesy of: Jean Jakoncic, AMX Beamline

## Slide 24: Pin/Gripper Image Analysis – Results – Image 4
Console Output:
Image 4:
perimeter: 3790.45496655
max: (1443, 1)
height: 821
extrema: {'B': (828, 822), 'R': (1447, 125),
'L': (492, 1), 'T': (492, 1)}
aspect ratio: 1.16301703163
area: 664209.0
min: (503, 1)
sum intensity: 35452804
width: 955
centroid: (974, 387)
mean intensity: 45.2172411374
Match Metrics:
Image Dissimilarity: 0.190836638543
Possible Kinks Detected
44 Possible Kink Points Detected: Adjust Gripper
Possible Kink Distance on R: 125.015998976
Possible Kink Distance on L: 157.003184681
Pin Not Mounted Correctly: Distance: 411
Images Courtesy of: Jean Jakoncic, AMX Beamline

## Slide 25: Pin/Gripper Time – 1-19 Images
Number of Images | Total Time | Average Time
1 | 0.544 | 0.544
2 | 0.751 | 0.3755
3 | 0.945 | 0.315
4 | 1.162 | 0.2905
5 | 1.361 | 0.2722
6 | 1.565 | 0.26083333
7 | 1.802 | 0.25742857
8 | 1.999 | 0.249875
9 | 2.192 | 0.24355556
10 | 2.429 | 0.2429
11 | 2.621 | 0.23827273
12 | 2.803 | 0.23358333
13 | 3.064 | 0.23569231
14 | 3.264 | 0.23314286
15 | 3.482 | 0.23213333
16 | 3.637 | 0.2273125
17 | 3.824 | 0.22494118
18 | 4.1 | 0.22777778
19 | 4.302 | 0.22642105
Chart: Average Time Per Photo
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
Avg | 0.544 | 0.3755 | 0.315 | 0.2905 | 0.2722 | 0.26083 | 0.25743 | 0.24988 | 0.24356 | 0.2429 | 0.23827 | 0.23358 | 0.23569 | 0.23314 | 0.23213 | 0.22731 | 0.22494 | 0.22778 | 0.22642
Chart: Total Time
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
Time | 0.544 | 0.751 | 0.945 | 1.162 | 1.361 | 1.565 | 1.802 | 1.999 | 2.192 | 2.429 | 2.621 | 2.803 | 3.064 | 3.264 | 3.482 | 3.637 | 3.824 | 4.1 | 4.302

## Slide 26: Crystal Rotational Alignment - AMX
Purpose:
Locate the Crystal
Center the Crystal in Goniostat
Plot as a function of angles the Y Pixel coordinate of Crystal during rotation
Images Courtesy of: Jean Jakoncic, AMX Beamline

## Slide 27: Crystal Rotational Alignment - AMX
Centering Crystal:
Images Courtesy of: Jean Jakoncic, AMX Beamline
Total Time (24 Img): 0.858s Average Time: 0.035s

## Slide 28: Conclusion
Computer Vision provides:
  Center Samples in Goniostat (ABBIX, IXS, etc.)
  Automated Robotic Mounting and Sample Detection (AMX)
  Assist in alignments of samples, crystals, and beams
  Discovers and reports information about objects within an image
  Prevent potential problems by alerting users of anomalies
With OpenCV 3.1.0 and the Intel IPP Library, all CV functions run at optimized speeds, providing the best computational results currently available.

## Slide 29: Future Plans - XPD
XPD X-Ray Diffraction Scoring Analysis:
  Discover Diffraction Circles
  Integrate Intensities
  Count Number of Circles
  Count Total Diffraction in each Frame
Images Courtesy of: Sanjit Ghose, XPD Beamline